# 3G/4G&WIFI Set Direction

The Enabled 3G/4G& WIFI Modules

1.3G：

CDMA2000:

EC156

EC1261

WCDMA:

E352

E173

E176G

E177

2.4G：

WCDMA(CUCC)：

E3272（华为）

IC161（VID=0x161c，PID=0xf010，6630 support）

3.WIFI：

RT3070 MT7601 8188eu、8188fu、8192cu、8192eu

## 一、3G Set

【Enable】：Must enabled

【Type】：Normally select auto

【access】：The access point of 3G. Different country not same.

【Number】：The number of 3G

【UserName】：The Username

【Password】：The password

【IP address】：

FOR China

CTCC-CDMA2000:

access ：ChinaNet

Number ：#777

UserName ：ctnet@mycdma.cn

Password ：vnet.mobi

CUCC-WCDMA:

access  ：3gnet

Number  ：*99#

UserName  ：无

Password  ：无

CMCC-TDS-CDMA

access   ：cmnet

Number   ：*99***1#

UserName  ：card

Password  ：card

Note: the above is the domestic operators 3G products corresponding settings information, only for domestic 3G product settings.

NOTE: The up info is just for china.

3G network card setup process

1. Reboot

2. Insert the module

3. Turn the device features 3G, Telecom selected EVDO or CDMA1.X,  Unicom please choose WCDMA

4. Wait for the dial-up IP address

Dial IP address appears when representatives of dial-up success, this time on behalf of telecommunications equipment has entered one APN LAN

And we are now working on the computer in our local area, we can not visit each other between the LAN, but the device within the LAN can access the public network resources.

This time can actually access the device, so the use of P2P WEB access to the equipment, or use the domain to apply a DDNS domain name to access the device.

Enter the serial device, you can discover the device can ping the external network IP, on behalf of the device has access to the Internet, but the device is within a certain APN LAN, external network can not see the device. Outside the network need to see the device by the device must be Excavators P2P, this is our cloud services.

Ps：

For Unicom, you should know,the address the you get through 3G card,maybe not public address.So you maybe still can not access the device through the IP. But you can use CLOUD ID  or  DDNS Domain to access it.

## 二、WIFI

The device can use WIFI module to connect to the router. And the client can connect to the device.

P 4.27 wifiSet

【Search】：Press search button can search out all the wireless router.

【Enable】：Must be enabled

【SSID】：The wireless LAN name

【Password】：The password of wireless router

【IP address】:The Ip address of device ，default：0.0.0.0

【SubMask】: The SubMask of device default：0.0.0.0

【GateWay】：The Gateway of device，default：0.0.0.0