Alarm linkage output description

When an alarm (motion detection, video loss, video occlusion, external alarm) is generated,Linkage external alarm to the corresponding alarm.

External alarm device connection

Description:

C and NO correspond to the DVR C and NO alarm output interface;

NOTE: The annunciator needs to be powered externally.

Extensions:

Alarm for the four-core alarm,one red and black for the two power lines，the remaining two lines for the alarm signal line,then the hard disk recorders C and NO is the alarm output.

1.Recording settings

Click the recording function in the video settings, the interface shown in Figure;

Description:

Check the alarm and check the two functions,when a corresponding alarm is generated,so the linkage to take effect;

If these alarms are not enabled, the video channel of the linkage video channel does not take effect.

2.Alarm linkage settings

Click the alarm function, enter the alarm type function settings, the interface is as follows:

Description:

Alarm function, including: motion detection, video occlusion, video loss, alarm input, alarm output, exception handling.

2.1 Motion Detection

Click the alarm function in the motion detection, the interface is as follows:

【Channel】 Select the channel to set the motion detection area;

【Enable】 Click ■, that is to open the motion detection function, select Enable, you can make the appropriate settings;

【Sensitivity】 According to the sensitivity, can be set to six files;

【Area】 Click to set into the area is divided into PAL16X11, pink area for the dynamic detection of detection area, black for the detection area;

【Disarm and Disarm Time】 During the set time range, the device will trigger the motion detection alarm signal, as shown in the figure below:

Note: You can set by week, but also a unified set, set four time periods per day. Select the time period before the check box ■, set the time to be effective.

【Interval】 In the set interval time, if there are multiple mobile detectors only trigger the alarm signal;

【Alarm Output】 When the motion detection signal is generated, set the external device to start the corresponding linkage alarm output port;

【Delay】: When the alarm is finished, the alarm will be stopped for a period of time, ranging from 10 to 300 seconds;

【Recording channel】 Select the required recording channel (can be selected repeatedly), when the alarm occurs, the system triggers the channel recording signal;

Note: For the linkage recording, you need to set in 【Record Setting】, in the corresponding time period, to start the detection of video.

【Tour】 selected ■, there is an alarm signal, the selected channel for single-screen round Tour preview,the interval of polling is set in 【System setting】> 【Polling setting】.

【Grab】 Select the required recording channel (can be selected repeatedly), when the alarm occurs, the system triggers the channel capture signal;

Note: To carry out linkage mapping, you need to set in 【Video Settings】, in the corresponding time period to start the detection of video.

【PTZ linkage】 When the alarm occurs, set the PTZ of the channel to be linked, as shown in the figure:

Note: For the PTZ, you need to set the preset point, cruise between points, round patrol and other parameters in 【shortcut menu】> 【PTZ control】.

【Video Delay】 After the alarm status is finished, the alarm recording will be stopped for a period of time, ranging from 10 to 300 seconds;

【Screen prompt】 On the local host screen, an alarm message dialog box will pop up;

【Send EMAIL】selected■，indicating that the alarm occurs at the same time send a message to notify the user;

Note: Send EMAIL, need to be in the [Network Services] in the appropriate settings.

【Buzz】 When the alarm happens, the device will send out two long beeps;

2.2 Video mask setting method: Refer to chapter "2.1 Motion detection".

2.3 Video loss setting method: Refer to chapter "2.1 Motion detection".

2.4 Alarm input setting method: Refer to chapter "2.1 Motion detection".

2.5 Alarm Output

Control the alarm output status of each channel, select ■ that the channel has alarm output. You can access the alarm output interface through the desktop shortcut menu, or in the 【main menu】>【 alarm function】> 【alarm output】.

【Configuration】 According to the configuration information, the output alarm signal;

【Manual】 No matter what state, select "Manual" button, the corresponding channel output alarm signal;

【Close】 No matter what state, select "Close" button, the corresponding channel does not output alarm signal;

【Status】 When the alarm output signal is generated, the box will display the check status.