The instructions on the digital channel

Open the equipment - the system Settings - open channel management - channel mode selection digital channels (hereinafter referred to as NVR), on the top of the box box, was determined, the equipment to restart...

Steps:

- log in device, click the right mouse button, in the main menu, click on the digital channels, can each channel (IPC)

- a digital channel interface (DO1) click enable, and click on add, the default configuration for

Can manually modify the device address, port, user name and password

- a digital channel interface, click on the enable, add, right click on the search can only search in the local area network (LAN) open (IPC) as shown in figure:

- search well, if you have any password IPC need to manually add password, then click ok:

- is determined, in the list of network configuration, configured the IPC before tick the box, click ok can monitor recently IPC (if video can't open, look at the first how much is the resolution of the IPC, to see whether the NVR support) :

(6) can be normal after monitoring, and view to the operation of the front IPC simple information