Email配置说明

1.Send Email when get alarm

Device can send email out when get alarm info if the configuration is setting

2.

Mailbox settings(1)

- 1.Main manual-->Internet service--->Email（163 for example）

- 2.SMTP:smtp.163.com

- Port：25

- SSL：If need

- 3.username： XXX@163.com  password：******

- 4.sender：XXX@qq.com

- subject：Input as you want

Email Set (2)

Email Set（3）

Configuration：The Ip and DNS should be right, or the email may can not send out.

3. Parameters Table

|  | smtp server | Port | SSL | username | pw |  |
| --- | --- | --- | --- | --- | --- | --- |
| google | smtp.gmail.com | 587/465 | Y | username | Email pw | Manually opened smtp |
| 163 | smtp.163.com | 25 | N | username | Authorization PW | Manually opened smtp |
| 126 | smtp.126.com | 25 | N | username | Email pw |  |
| qq | smtp.qq.com | 25 | N | username | Authorization PW | Manually opened smtp |
| yahoo | smtp.mail.yahoo | 465 | Y | username | Email pw | Manually opened smtp |
| sohu | smtp.sohu.com | 25 | N | username | Email pw |  |
| sina | smtp.sina.com | 25 | N | username | Email pw | Manually opened smtp |
| hotmail | smtp.office365.com smtp.live.com | 587/25 | Y | username | Email pw | Manually opened smtp |
| AOL | smtp.aol.com | 25 | N | username | Email pw |  |
| GMX | smtp.gmx.com | 25 | N | username | Email pw |  |

Note：1.Some mailbox need to be open smtp by hand。

- The time of device must be right

- Some mailbox should open SSL like GMail

When you test gmail, the time should be large than 2000, or the certificate will be error.

4.Linkage set

For example: When detect the motion alarm, the email will be send.

5.Email

6. Hotmail/outlook Test Example

Log in to hotmail / outlook account to configure SMTP.

If you are applying for an account for the first time, you need to send an email by email.

Device settings

Smtp server: smtp.live.com/smtp.office365.com

Port:587/25  (if 25 can’t, use 587)

SSL:Enable

7.Gmail Test Example

- Open IMAP

- Device setting

Smtp server: smtp.gmail.com

Port:587/465  (if 465 can’t, use 587)

SSL:Enable

- Mail Test

If the following prompt appears.

  - 535-5.7.8 Username and Password not accepted. Learn more at 535 5.7.8  https://support.google.com/mail/?p=BadCredentials x7sm6962664pfp.93 – gsmtp

https://myaccount.google.com/security

534-5.7.14 <https://accounts.google.com/signin/continue?sarp=1&scc=1&plt=AKgnsbu

https://accounts.google.com/DisplayUnlockCaptcha

Attention:

When you test gmail, the device time should be large than 2000, or the certificate will be error.