Port mapping instructions

Premise

- DVR / NVR / IPC has access to local area network, and the local area network can access the public network

- The router supports UPNP, and this function is enabled

Different models of router settings upnp Please refer to the router instructions

The default administrative address of the TP-LINK series router is 192.168.1.1，account is admin ,password is admin, log on to the router's management interface.

Method to realize:

- UPNP automatic mapping (TP-LINK series routers as an example)

Check that the local DVR does not conflict with the IP-mac address of other devices in the LAN

（1）Open the main menu - System Settings - Network Services - UPNP interface.

- Enable option √ - OK. Wait for 1-2 minutes and wait for the DVR to get to the mapped port

- 1-2 minutes and then open the UPNP configuration interface, as shown, that upnp mapping has been successful

In the router, you can view the mapping of the current device:

As above operation can also be in the local network service, synchronous display.

At this point you can use the "router IP: external network port," the address form in the public network to access the DVR

http://122.234.233.104：85

一、Manual mapping

(1)Click on the router's forwarding rule <Virtual Server> to add a new entry.

(2)Port mapping settings are as follows: You can manually add port mapping, the device side with the mapping port number.（Do not add a port and the LAN port mapping conflict）

Such as the device's IP address is 192.168.1.112, the external network port number is 99 (that is the service port).

- The management interface of the router.Click on the router's forwarding rule <Virtual Server> to add a new entry.

- Service port number：99，IP address：192.168.1.112。-save。

(4)Open the main menu - System Settings - Network Settings - HTTP port to 99 - OK.（Default 80）

(5)Log in to the router directly at the Web-side IP:service port number，122.234.233.104:99 you can log in to the Web-side interface.

Thanks for reading!