Snapshot configuration steps：

# 一、Hard disk settings

1、【main menu】—>【Administrative Tools】—>【Hard disk management】—>【Partition】

2、In the partition interface, enter the size of the capture partition, the system will automatically record the partition and the capture partition to allocate space (unit is MB)

3、Prompt to complete the partition, restart. Click 【OK】

4、After the restart there will be a snapshot disk management (the following 1-2 is the image partition)

- Picture storage settings

Set the parameters of the monitoring channel. The first time, the system is set to 24 hours continuous capture.Available on【main menu】>【Recording function】>【Image storage】make the appropriate settings.

【Aisle】Select the corresponding channel number for channel settings, unified all channel settings can choose all;

【Pre-shot】Before the recording state, set the number of pre-shot pictures, the default is 5

【Recording function】Set the recording status, there are three states: configuration, manual and closed;

Configuration: According to the settings (normal, detection and alarm) recording type and recording time period to achieve capture;

Manual: Regardless of the status of the current channel, select the "Manual" button, the corresponding channel has a capture function;

Off: Regardless of the state of the current channel, when the "Close" button is selected, the corresponding channel is stopped.

【period】Set the time range for normal recording to start the image storage function within the set time range.

【Types】Set the type, there are three types: normal, detection, alarm.

【Recording type】Set the recording type, there are three types: normal, detection, alarm.

Normal: The captured image is always taken during the set time period

Detection: During the set time period, when motion detection, video

occlusion and video loss alarm are triggered, and the corresponding alarm function is set to open the capture function, the signal can be captured.

Alarm: Trigger external alarm signal within the set time period, and          "Alarm Input" function is set to open the capture function, trigger alarm signal can capture.

# 三、DNS settings

1、【main menu】—>【System Settings】—>【Network settings】

2、Set the correct IP gateway DNS and backup DNS and other network parameters (the figure below only for example), save.

Example:Ip address 192.168.1.128

Subnet Mask 255 255 255 0

The default gateway 192.168.1.1

Preferred DNS 192.168.1.1

Spare DNS 8.8.8.8

# 四、Internet service

1、【main menu】—>【System Settings】—>【Internet service】—>【EMAIL Settings】

2、Select【Enabled】Fill in the correct Email information

User Name: The user name of the mailbox you requested

Password: The password of the mailbox you requested

From: Your full email address

To: You can have up to 3 recipients separated by ";" (semicolon), and the recipient can be the same as the sender

Subject: You can set the subject of the message according to your needs

The other according to the above can be filled.

# Note: gmail requires SSL encryption, so "this server requires a secure connection (SSL)" must be selected, the rest determined by the Email

# 五、Alarm settings（To mobile detection, for example, video occlusion, video loss, the same alarm input)

1. Select the channel number to be set

2, select 【Enable】

3, select the channel number to capture

4, select 【send EMAIL】

Note: If you want to use the capture function, you must set the above five steps, and ensure that each item is set correctly